## Slide 1: Lithium-Ion Batteries
Electrochemical energy storage devices
Secondary battery
Social awareness
Climate changes due to the CO2 emissions
Electric vehicles (EVs)
Energy storage for solar energy

## Slide 2
Challenges
Raw materials
Overall production cost
High production ,huge waste
Global LIBs recycling market 1,11,783 t in 2018
Expected to reach approximately 6,41,595 t in 2025
less than 5% is recycled

## Slide 3: How Can We Manage LIBs Waste
Second life use
For house hold works or backup system.
Buried in land
Damage to soil, explosive
Burned
Produce poisonous gases.
Recycle in closed loop process
recover the metals like Co, Ni, Li, etc.

## Slide 5
Battery Component | % w/w | Used Material
Case | 25% | Steel/plastics
Cathode | 27% | LiNixMnyCo2O2
Anode | 17% | Graphite
Current Collectors | 13% | Cu and Al
Electrolyte | 10% | LiPF6
Separator | 4% | Microporous Polypropylene
Binder | 4% | Polyvinylidene Difluoride

## Slide 6: Process For Recycling of Lithium Ion Batteries

## Slide 7
Black Mass Producing Unit
(shredding plant)
Feed
Lithium ion battery (pouch cell) ( let 100 kg)
Product
Black mass (cathode and anode material) (55.15 kg)
Al, Cu and separator (38.86 kg)
Electrolyte and waste (11.35 kg)

## Slide 9
PLANT PROCESSES
Discharge the batteries
NaCl solution OR electrical load
Cutter
Slowest step therefore rate determination step
Heating and Mixer Tank
Fumes of electrolyte, binder loss it properties and black mass separate
Sieving machine
Separate Al and Cu from black mass (mesh size 0.6mm)

## Slide 10
Electrostatic separator
Separate Cu and Al
Cyclone separator
Separate solid particle (black mass) from air (electrolyte fumes)
Condenser unit
Condense electrolyte fumes
Scrubber
Dry scrubber using HEPA or Carbon filters.

## Slide 11
Metal Extraction Unit
Metal extraction (hydrometallurgical methods)
FEED
Black mass
PRODUCT
Graphene
Cobalt sulfate
Copper sulfate
Nickel sulfate

## Slide 12
REACTOR 1
Working capacity = 100liters (let)
Inlet = water H2SO4 Black mass
Time 2 hrs.
FILTERATION UNIT
Filtration Press
Inlet leached residue
extract graphene(mesh size 25 micron)

## Slide 13
REACTOR 2
Inlet = leach liquor + H2SO4
Outlet = Selective Extraction(stripping) of NiSO4 and
CuSO4
REACTOR 3
Inlet = leached liquor
Outlet = CoSO4 (ppt)

## Slide 14
FUTURE SCOPE
Increase purity level (Electrolysis)
Make continuous process
Find application of derived material
for ex Graphene - graphene oxide - supercapacitor and anticorrosion.

## Slide 15: THANK YOU